## Slide 1: GridPACK™ Framework for Developing Power Grid Applications for HPC Platforms
Bruce Palmer, Bill Perkins, Kevin Glass, Yousu Chen, Shuangshuang Jin, Ruisheng Diao, Mark Rice, David Callahan, Steve Elbert, Henry Huang

## Slide 2: Objective
Develop a framework to support the rapid development of power grid software applications on HPC platforms
Extend the penetration of HPC in power grid modeling
Provide high level abstractions for often used motifs in power grid applications
Reduce the amount of explicit communication that must be handled by developers
Allow power grid application developers to focus on physics and algorithms and not on parallel computing

## Slide 3: Approach
Develop software modules that encapsulate commonly used functionality in HPC power grid applications
Setup and distribution of power grid networks
Input/Output
Mapping from grid to distributed matrices
Parallel solvers
Incorporate advanced parallel libraries whenever possible
  PETSc, ParMETIS
GridPACK™ is currently available as a set of C++ software modules and classes

## Slide 4
Core Data Objects
Power Grid Network and Fields
Matrices and Vectors
Network Components
Neighbor Lists
Matrix Elements
Application Factory
Solver
Math and Solver Module
PETSc
Mapper
Network Module
Ghost Exchanges
Partitioning
Matrix and Vector Module
PETSc
Applications
Import Module
PTI Formats
Dictionary
Export Module
Serial IO
PTI Formats
GridPACK™ Framework
Configure Module
XML
GridPACK™ Software Stack
Utilities
Errors
Logging
Profiling

## Slide 5: Major GridPACK™ Modules
Network: Manages the topology, neighbor lists, parallel distribution and indexing. Acts as a container for bus and branch components
Bus and Branch components: define the behavior and properties of buses and branches in network. These components also define the matrices that can be generated as part of the simulation
Factory: Manages interactions between network and the components

## Slide 6: Application Flow Diagram
Configuration File
Topology File
Configure Module
Import Network
Network Module
Partition
Network Object
Application
Solver
Mapper
Math Module
Export Network
Output File
Factory
Network Object
Network topology, simple fields
Network topology, network components
Network Component

## Slide 7: Building the GridPACK™ Library
GridPACK™ requires the following libraries
  MPI (Message Passing Interface): This is the standard parallel communication library and is available on most parallel platforms. It can be downloaded from several sources and built on most Linux workstations
  Global Arrays: This can be downloaded from http://hpc.pnl.gov/globalarrays/ and built on most Linux platforms.
  PETSc: This library supports most of the matrix and solver capability in GridPACK™. It can be downloaded and built from http://www.mcs.anl.gov/petsc/.
  Boost: The Boost libary supplies several extensions to C++ that are used throughout GridPACK™. Boost can be downloaded from http://www.boost.org/.
  Parmetis: This library supplies the partitioning function in PETSc. It can usually be build within PETSc but if it has not, then it can be downloaded from http://glaros.dtc.umn.edu/gkhome/metis/parmetis/overview and built separately

## Slide 8: MPI
MPI is ubiquitous on parallel platforms and is usually already built. Linux workstations probably don’t have it installed but it can be downloaded from several sources and built fairly easily
  MPICH: available from http://www.mpich.org/
  MVAPICH/MVAPICH2: available from http://mvapich.cse.ohio-state.edu/
  OPENMPI: available from http://www.open-mpi.org/
Each of these implementations has its own pluses and minuses, but any of them will be suitable for most GridPACK™ applications
Follow the instruction for each package to build it

## Slide 9: Global Arrays
GA supplies the internal communication layer for several GridPACK™ modules
GA can be built on top of MPI or it can use native ports on Infiniband and DMAPP (Cray) networks
GA uses an autoconfig build to configure the library and then build it using make
  Building GA on workstation using 2-sided MPI
  configure --with-mpi-ts --enable-cxx \
  --disable-f77 --enable-i4 \
  --prefix=$(GA_HOME)
Use different option for --with-mpi-ts on different platforms

## Slide 10: PETSc
PETSc is the most complicated library to build
A typical configure line looks like
./configure \
PETSC_ARCH=arch-linux2-complex-opt --with-prefix=./ \
--with-mpi=1 --with-cc=mpicc --with-fc=mpif90 \
--with-cxx=mpicxx --with-c++-support=1 --with-c-support=0 \
--with-fortran=0 --with-scalar-type=complex \
--with-fortran-kernels=generic --download-superlu_dist \
--download-parmetis --download-metis \
--download-f2cblaslapack=1 --with-clanguage=c++ \
--with-shared-libraries=0 --with-dynamic-loading=0 \
--with-x=0 --with-mpirun=mpirun --with-mpiexec=mpiexec \
--with-debugging=0

## Slide 11: PETSc (cont)
PETSC_ARCH is a user-defined name that identifies this particular build
After configuring, the PETSc build will lead you through the make process. Follow the commands coming from the build
If Metis and Parmetis are built as part of the PETSc libraries then they do not need to be downloaded and built separately. This guarantees consistency between compilers and other environmental settings across the PETSc and Parmetis libraries.
This example includes both Parmetis and SuperLU

## Slide 12: Boost
The Boost extensions to C++ are widely available
The Boost libraries can be configured and built using the commands
Some commands may differ depending on platform
echo "using mpi ;" > ~/user-config.jam
sh ./bootstrap.sh \
--prefix="$prefix" \
--without-icu \
--with-toolset=gcc \
--without-libraries=python,log
./b2 -a -d+2 link=static stage
./b2 -a -d+2 link=static install
rm ~/user-config.jam

## Slide 13: ParMetis
As mentioned above, it is better to build ParMetis (and Metis) as part of PETSc. However, it can be built standalone
To get ParMetis to build with older GNU compilers, run the following command first
  sed -i.org -e \
  's/-Wno-unused-but-set-variable//g‘ \
  metis/GKlib/GKlibSystem.cmake
This removes some newer compiler options

## Slide 14: ParMetis (cont)
To build Metis, execute the following commands (starting in the top level directory)
  cd metis
  make config prefix=/my/install/directory
  make
  make install

## Slide 15: ParMetis (cont)
After building Metis, execute the following commands
  cd ..
  make config cc=mpicc cxx=mpicxx \
  prefix=/my/install/directory
  make
  make install
Run some tests to check if build is okay
  cd Graphs
  mpirun –np 4 ptest rotor.graph rotor.graph.xyz
  mpirun –np 4 ptest rotor.graph

## Slide 16: Configure GridPACK™
Create a directory that will contain the GridPACK™ build and cd into it
Configure GridPACK™ using cmake (RHEL5 example)
cmake -Wno-dev \
-D BOOST_ROOT:STRING=‘/top/level/boost/directory’ \
-D PETSC_DIR:STRING=‘/top/level/petsc/directory' \
-D PETSC_ARCH:STRING='arch-linux2-cxx-opt' \
-D PARMETIS_DIR:STRING='/parmetis/lib/directory’ \
-D GA_DIR:STRING=‘/top/level/ga/directory’ \
-D MPI_CXX_COMPILER:STRING=‘/mpicxx/location’ \
-D MPI_C_COMPILER:STRING=‘/mpicc/location’ \
-D MPIEXEC:STRING=‘/mpiexec/location’ \
-D CMAKE_BUILD_TYPE:STRING="Debug" \
-D CMAKE_VERBOSE_MAKEFILE:BOOL=TRUE \
..
This points to GridPACK™ source directory

## Slide 17: Configuring GridPACK™ (cont)
The string corresponding to “PETSC_ARCH should match the PETSC_ARCH string used in configuring the PETSC library
The options for CMAKE_BUILD_TYPE are
  DEBUG (not optimized, built with –g)
  RELEASE (optimized)
  RELWITHDEBINFO (optimized but built with –g)
After configuring, type “make” in the build directory to build all libraries and applications. Individual libraries and applications can be built by cd’ing into those directories and typing “make”

## Slide 18: BaseNetwork Class
Template class that can be created with arbitrary user-defined types for the buses and branches
  BaseNetwork<MyBus, MyBranch>
Implements partitioning of network between processors
  Create highly connected sub-networks on each processor with minimal connections between processors
Implements data exchanges between buses and branches on different processors
Manages indexing of network components

## Slide 19: Instantiate a Network
#include “gridpack/network/BaseNetwork.hpp”
#include “gridpack/applications/myapp/mycomponents.hpp”
typedef gridpack::network::BaseNetwork
<gridpack::myapp::MyBus,
gridpack::myapp::MyBranch> MyNetwork;
boost::shared_ptr<MyNetwork> network(new MyNetwork);
// Create a network object that has the application-specific
// bus and branch models associated with it. The network will
// also have DataCollection objects on each bus and branch.
// At this point, the network is just a container and has no
// topology or data

## Slide 20: Parser Module
Currently, only PTI version 23 format is supported.
Work is under way to develop a parser based on more generic GOSS formats
// Constructor
PTI23_parser<MyNetwork>::PTI23_parser(
boost::shared_ptr<MyNetwork> network);
// Import external network configuration file and generate
// network topology
void parse(const std::string &filename)

## Slide 21: Create Network from External File
#include “gridpack/parser/ParserPTI.hpp”
:
gridpack::parser::PTI23_parser<MyNetwork> parser(network);
parser.parse(“location_of_PTI_file”);
// The network topology now exists and the data
// collection objects on each bus and branch are filled
// with parameters from the PTI file. The network is
// NOT, however, distributed in an optimal way at this
// point. Also, no ghost buses or ghost branches have
// been added to the network yet, so most calculations
// not possible

## Slide 22: Network Topology
Bus
Branch

## Slide 23: Network Data
Data Collection Objects on Buses
Data Collection Objects on Branches

## Slide 24: DataCollection Objects
Each bus and each branch has its own DataCollection object
DataCollections are lists of key-value pairs representing parameters from network configuration file
,
=
Param1:Value1
Param2:Value2
Param3:Value3
:

## Slide 25: Network Components
Uninitialized Bus Component
Uninitialized Branch Component

## Slide 26: Partition Network
// Invoke the partition function
network->partition();
// Network has been properly distributed among
// processors, ghost buses and ghost branches have been
// added to the network, and global indices have been
// set. Local neighbor lists and indices for the ends
// branches have also been set. Network is almost ready
// for calculations

## Slide 27: Partitioning the Network
Process 0
Process 1

## Slide 28: Process 0 Partition
Process 0
Ghost Buses and Branches

## Slide 29: Process 1 Partition
Process 1
Ghost Buses and Branches

## Slide 30: Other Base Network Class Methods
// Return number of buses and branches on this process
// (including ghost buses and branches)
int numBuses(void);
int numBranches(void);
// Get local index of reference bus (return -1 if
// reference bus is not on this process)
int getReferenceBus(void) const;
// Return true if bus or branch is local to the process,
// return false for ghost buses and branches
bool getActiveBus(int idx);
bool getActiveBranch(int idx);
// Return pointer to bus or branch object corresponding
// to local index idx
boost::shared_ptr<MyBus> getBus(int idx);
boost::shared_ptr<MyBranch> getBranch(int idx);

## Slide 31: Base Network Class
// Return pointer to DataCollection objects associated
// with bus or branch at local index idx
boost::shared_ptr<gridpack::component::DataCollection>
getBusData(int idx);
boost::shared_ptr<gridpack::component::DataCollection>
getBranchData(int idx);
// Remove all ghost buses and branches from the network
void clean(void);
// Set up data structures for exchanges to ghosts buses
// and branches
void initBusUpdate(void);
void initBranchUpdate(void);
// Send data to ghost buses and branches
void updateBuses(void);
void updateBranches(void)

## Slide 32: Factories
Factories are used to manage interactions between the network and individual network components
Factories perform some basic initialization functions
Factories are designed to set up the system so that it can be used in calculations. They guarantee the all bus and branch objects are in the correct state for generating the matrices and vectors needed for solving the problem
Factories can be used to change the state network components
A primary motif in factory methods is that they loop over all bus and branch objects and invoke methods on them

## Slide 33: Base Factory Class
// Constructor
BaseFactory<MyNetwork>::BaseFactory(
boost::shared_ptr<MyNetwork> network);
// The “load” operation takes all the data from the
// data collection objects and moves them into the
// corresponding bus and branch components using the
// load functions that have been defined in the
// individual bus and branch classes
virtual void load(void);
// Set up lists of pointers in each component to
// neighbors of all buses and branches in the
// network as well as assigning internal indices used
// by other GridPACK™ components
virtual void setComponents(void);

## Slide 34: Base Factory Class
// Set up internal buffers so that data exchanges to
// fill up ghost branches and ghost buffers will work.
// To exchange data, users need to put the data in the
// component’s exchange buffer and then invoke a bus
// or branch ghost exchange in the network
virtual void setExchange(void);
// Invoke the setMode method on all bus and branch
// components in the network. The mode can be used to
// control the behavior of the network components at // different stages of the calculation
virtual void setMode(int mode);

## Slide 35: Create a New Factory
Class MyFactory
: public gridpack::factory::BaseFactory<MyNetwork> {
MyFactory(MyNetworkPtr network);
~MyFactory();
MyFactoryMethod1(…);
MyFactoryMethod2(…);
:
:
}

## Slide 36: Example of a Factory Method
/**
* Generic method that invokes the "load" method
* on all branches and buses to move data from
* the DataCollection objects on the network into the
* corresponding buses and branches
*/
void gridpack::factory::BaseFactory<MyNetwork>::load(void)
{
int numBus = p_network->numBuses();
int numBranch = p_network->numBranches();
int i;
// Invoke load method on all bus objects
for (i=0; i<numBus; i++) {
p_network->getBus(i)->load(p_network->getBusData(i));
}
// Invoke load method on all branch objects
for (i=0; i<numBranch; i++) {
p_network->getBranch(i)->load(p_network->getBranchData(i));
}
}

## Slide 37: Initialize Components
Use data in Data Collections to initialize bus and branch components via the load method

## Slide 38: Initialize Network Components
#include “gridpack/applications/myapp/MyFactory.hpp
:
gridpack::myapp::MyFactory factory(network);
// Initialize components with data from DataCollection
// objects
factory.load();
// Set up internal indices used by mappers to create
// matrices and vectors and set pointers for
// neighboring buses and branches
factory.setComponents();
// Set up buffers for ghost exchanges
factory.setExchange();

## Slide 39: Components
All components are derived from the MatVecInterface class and the BaseComponent class
Bus components are derived from the BaseBusComponent class
Branch components are derived from the BaseBranchComponent class

## Slide 40: Component Class Hierarchy
MatVecInterface
BaseComponent
BaseBusComponent
BaseBranchComponent
AppBusComponent
AppBranchComponent

## Slide 41: The MatVecInterface
Designed to allow the GridPACK™ framework to generate distributed matrices and vectors from individual bus and branch components
Buses and branches are responsible for describing their individual contribution to matrices and vectors
Buses and branches are NOT responsible for determining location in matrix or vector and are NOT responsible for distributing matrices or vectors

## Slide 42: Data Type
Matrices and vectors are assumed to be complex
ComplexType used for everything, including real values (a real number is just a complex number with the imaginary part set to zero)

## Slide 43: Diagonal MatVecInterface
// Return the size of matrix block on the diagonal.
// Usually implemented on bus components. This function
// returns false if the component does not contribute
// anything to the matrix
virtual bool matrixDiagSize(int *isize,
int *jsize) const
// Return the values of the block in row-major order.
// Return false if component does not contribute to matrix
virtual bool matrixDiagValues(ComplexType *values)

## Slide 44: Off-diagonal MatVecInterface
// Return the size an off-diagonal matrix block
// contributed by the component. This function returns
// false if no values are contributed by component. These
// functions are usually implemented on branches. The
// Forward function is called for an ij pair when i
// corresponds to the “from” bus defining a branch.
// The Reverse function is called when i corresponds
// to the “to” bus
virtual bool matrixForwardSize(int *isize,
int *jsize) const
virtual bool matrixReverseSize(int *isize,
int *jsize) const
// Return the values of off-diagonal matrix block.
// Values are in row-major order.
virtual bool matrixForwardValues(ComplexType *values)
virtual bool matrixReverseValues(ComplexType *values)

## Slide 45: Vector MatVecInterface
// Return the block size of component contribution to
// a vector. Return false if a component does not
// contribute to vector
virtual bool vectorSize(int *isize) const
// Return the values of the vector block contributed
// by component
virtual bool vectorValues(ComplexType *values)

## Slide 46: BaseComponent
This class provides a few methods that are needed by all network components (bus or branch)
Provides methods for moving data from DataCollection objects to components and sets up buffers used for ghost bus and ghost branch exchanges
Provides a mechanism for changing component behavior so that different matrices can be extracted from components during different phases of the calculation

## Slide 47: BaseComponent
// These methods need to be redefined in application
// components. Default implementations are all no-ops
// Load data from DataCollection object into component
virtual void load(const shared_ptr<DataCollection> &data)
// Return the size of the buffer needed for data exchanges
// Note that all bus components must return the same value
// for this function and all branch components must return
// the same value
virtual int getXCBufSize(void)
// Assign the location of the data exchange buffer to an
// internal component pointer. This buffer is allocated
// and deallocated by the network
virtual void setXCBuf(void *buf)

## Slide 48: BaseComponent
// Write out a single string describing current state of
// the component. The character string “signal” can be used
// to control the behavior of the component. Return false
// if no string is being returned. This functionality is
// used in the serialIO module
virtual bool serialWrite(char *string, char *signal)

## Slide 49: BaseComponent::setMode
Each bus and branch component should have an internal mode variable corresponding to an enumerated type
Different values of the mode variable can generate different behaviors. For example, the network components in a power flow application must be able to generate both the Y-matrix and the Jacobian for a powerflow calculation
  If the mode is set to “YBus”, the MatVecInterface functions return values appropriate for creating the Y-matrix
  If the mode is set to “Jacobian”, the MatVecInterface functions return values appropriate for generating the Jacobian matrix used in the power flow equations
// Set internal behavior of component by specifying a “mode”
void setMode(int mode)

## Slide 50: BaseBusComponent
Provides methods that are needed by all bus component implementations
Sets up lists of branches that are attached to the bus and buses that are attached via a single branch
Keeps track of the reference bus

## Slide 51: BaseBusComponent
// Get pointers to branches that are connected to bus
void getNeighborBranches(vector<shared_ptr
<BaseComponent> > &nghbrs) const
// Get pointers to buses that are connected to bus via
// a single branch
void getNeighborBuses(vector<shared_ptr
<BaseComponent> > &nghbrs) const
// If bus is reference bus, set status to true
void setReferenceBus(bool status)
// Return true if this bus is reference bus
bool getReferenceBus(void) const

## Slide 52: BaseBranchComponent
Provides methods that are needed by all branch component implementations
Keeps track of the buses at each end of the branch and makes these available to the application

## Slide 53: BaseBranchComponent
// Get pointers to buses at either end of the branch.
// Bus 1 refers to the “from” bus and bus 2 refers to
// the “to” bus
shared_ptr<BaseComponent> getBus1(void) const
shared_ptr<BaseComponent> getBus2(void) const

## Slide 54: DataCollection Objects
Every bus and branch in the network has an associated DataCollection object
The DataCollection object is a container for key-value pairs of parameters associated with a particular bus or branch
Different buses and branches can contain different numbers of key-value pairs and different types of key-value pairs
If a bus or branch has a list of values associated with the same key, then these can be indexed
Key-value pairs are usually added to the DataCollection objects when the network is read in from a network configuration file

## Slide 55: Data Collection Structure
double key1:value1
int key2:value2
bool key3:value3
double key4:value4
double key5[0]:value5[0]
double key5[1]:value5[1]
double key5[2]:value5[2]
DataCollection instance

## Slide 56: DataCollection Names
Names assigned by parser are defined in the dictionary.hpp file
/**
* Non-blank alphanumeric branch circuit identifier
* type: string
*/
#define BRANCH_CKT “BRANCH_CKT”
/**
* Branch resistance; entered in pu
* type: real float
*/
#define BRANCH_R “BRANCH_R”
/**
* Branch reactance; entered in pu
* type: real float
*/
#define BRANCH_X “BRANCH_X”

## Slide 57: DataCollection Accessors
bool getValue(char *name, int *value);
bool getValue(char *name, long *value);
bool getValue(char *name, bool *value);
bool getValue(char *name, std::string *value);
bool getValue(char *name, float *value);
bool getValue(char *name, double *value);
bool getValue(char *name, gridpack::ComplexType *value);
bool getValue(char *name, int *value, int idx);
bool getValue(char *name, long *value, int idx);
bool getValue(char *name, bool *value, int idx);
bool getValue(char *name, std::string *value, int idx);
bool getValue(char *name, float *value, int idx);
bool getValue(char *name, double *value, int idx);
bool getValue(char *name, gridpack::ComplexType *value,
int idx);

## Slide 58: Mapper
Provide a flexible framework for constructing matrices and vectors representing power grid equations
Hide the index transformations and partitioning required to create distributed matrices and vectors from application developers
Developers can focus on the contributions to matrices and vectors coming from individual network elements

## Slide 59: Mapper
1
2
3
4
5
6
7
8
12
11
10
9

## Slide 60: Matrix Contributions from Components
1
2
3
4
5
6
7
8
12
11
10
9
No matrix contribution
No matrix contribution
No matrix contribution

## Slide 61: Distribute Component Contributions and Eliminate Gaps

## Slide 62: Matrix Mapper Interface
// Instantiate a new mapper that creates a matrix from
// bus and branch components on the network
FullMatrixMap<MyNetwork>::FullMatrixMap(
shared_ptr<MyNetwork> network);
// Create a matrix from the network
shared_ptr<Matrix> mapToMatrix(void);
// Reset matrix based on current network values
void mapToMatrix(shared_ptr<Matrix> &M);

## Slide 63: Vector Mapper Interface
// Instantiate a new mapper that creates a vector from
// bus components on the network
BusVectorMap<MyNetwork>::BusVectorMap(
shared_ptr<MyNetwork> network);
// Create a vector from the network
shared_ptr<Vector> mapToVector(void);
// Reset vector based on current network values
void mapToVector(shared_ptr<Vector> &V);
// Push current values in vector back into buses
void mapToBus(Vector &vector);

## Slide 64: Mapper Behavior
The matrix or vector that is produced by a mapper is controlled by
  The functions that are implemented in the MatVecInterface by the application developer
  The current value of the mode variable. If the application needs to create different matrices or vectors based on different modes, then separate mappers should be created for each mode
  When calling any of the mapper functions, the mode should always be set to the same value as the mode that was in place when the mapper was created

## Slide 65: Math Module
The math module is a wrapper on top of a parallel solver library. It supports
  Distributed sparse and dense matrices and distributed vectors
  Basic manipulations of matrices and vectors, e.g. matrix additions, matrix-vector multiplication, scaling of matrices, creation of identity matrix, etc.
  Linear solvers that support different algorithms and preconditioners for solving the matrix equation Ax=b
  Nonlinear solvers

## Slide 66: Math Library
// Initialize math library. Call any initialization
// routines that are necessary and read in any
// configuration files. Currently, PETSc options are
// listed in a gridpack.petscrc file. This is where
// preconditioners and other PETSc configuration
// parameters are specified.
extern void Initialize(void);
// Is math library initialized?
extern bool Initialized(void);
// Shut down math library
extern void Finalize();

## Slide 67: Vector Class
// Specify parallel configuration and local contribution
// to vector in constructor
Vector(const parallel::Communicator &comm,
const int &local_length);
// Accessors for vector properties
int size(void) const;
int localSize(void) const;
void localIndexRange(int &lo, int &hi) const;

## Slide 68: Distributed Vector Storage
Process 0
Process 1
Process 2
Process 3
Process 4
Process 5
Vectors are distributed in contiguous segments between processes

## Slide 69: Vector Class
// Set vector elements
void setElement(const int &i, const ComplexType &x);
void setElements(const int &n, const int *i,
const ComplexType *x);
// Access vector elements
void getElement(const int &i, ComplexType &x) const;
void getElements(const int &n, const int *i,
ComplexType *x) const;
// Indicate vector is ready to use
void ready(void);

## Slide 70: Basic Vector Operations
// Basic operations that can be performed on vectors
void zero(void);
void fill(const ComplexType &v);
ComplexType norm1(void) const; // L1 norm
ComplexType norm2(void) const; // L2 norm (standard)
void scale(const ComplexType &x);
void add(const Vector &x, const ComplexType &scale = 1.0);
void equate(const Vector &x);
void reciprocal(void);

## Slide 71: Matrix Class
// Specify dimensions and storage format of matrix in
// constructor.
Matrix(const parallel::Communicator &dist,
const int &local_rows,
const int &cols,
const StorageType &storage_type=Sparse);
// Accessors for matrix properties
int rows(void) const;
int localRows(void) const;
void localRowRange(int &lo, int &hi) const;
int cols(void) const;

## Slide 72: Distributed Matrix Storage
Process 0
Process 1
Process 2
Process 3
Process 4
Process 5
Matrices are laid out in row blocks

## Slide 73: Matrix Class
// Set matrix elements
void setElement(const int &i, const int &j,
const ComplexType &x);
void setElements(const int &n, const int *i,
const int *j, const ComplexType *x);
// Access matrix elements
void getElement(const int &i, const int &j,
ComplexType &x) const;
Void getElements(const int &n, const int *i,
const int *j, ComplexType *x) const;
// Indicate matrix is ready
void ready(void);

## Slide 74: Basic Matrix Operations
// Basic operations that can be performed on matrices
void equate(const Matrix &A);
void scale(const ComplexType &x);
void multiplyDiagonal(const Vector &x);
void add(const Matrix &A);
void identity(void);
void zero(void);
// Matrix-Vector operations
extern Matrix *add(const &A, const &B);
extern Matrix *transpose(const Matrix &A);
extern Vector *column(const Matrix &A, const int &cidx);
extern Vector *diagonal(const Matrix &A);
extern Matrix *multiply(const Matrix &A, const Matrix &B);
extern Vector *multiply(const Matrix &A, const Vector &x);

## Slide 75: Linear Solver
// Solve equation using an instance of a LinearSolver
LinearSolver(const Matrix &A);
void solve(const Vector &b, Vector &x) const;
void configure(CursorPtr cursor);
// Most of the solver functionality can be accessed by
// requesting it in the input deck
<LinearSolver>
<PETScOptions>
-ksp_view
-ksp_type richardson
-pc_type lu
-pc_factor_mat_solver_package superlu_dist
-ksp_max_it 1
</PETScOptions>
</LinearSolver>

## Slide 76: Configure
Configure is designed to take user input, in the form of an XML-based input file, and transfer that information to any parts of the code that might need it. Configure is designed to handle relatively limited amounts of data, it is not designed for handling large data objects like the network. Examples of user input include
  Location of network configuration file
  Type of solvers to use
  Solution parameters such as convergence tolerance, maximum number of iterations, etc.
  Control parameters for different types of data output

## Slide 77: Configuration Module
// Access common instance of configuration module,
// shared across all modules
static Configuration* configuration()
// Open external configuration file
bool open(std::string file, Communicator comm)
typedef Configuration Cursor
// Set the “cursor” in the Configuration object so
// that it only looks at key-value pairs within the
// block delimited by “key”
Cursor* getCursor(std::string key)

## Slide 78: Configuration Accessors
// Return default value if no value for that key is
// set in input file
bool get(std::string, bool default_value)
int get(std::string, int default_value)
double get(std::string, double default_value)
std::string get(std::string,
std::string default_value)
std::vector<double> get(std::string,
std::vector<double> default_value)
// Return value for key, value of function is
// false if no value found
bool get(std::string, bool *value)
bool get(std::string, int *value)
bool get(std::string, double *value)
bool get(std::string, std::string *value)
bool get(std::string, std::vector<double> *value)

## Slide 79: Input File example
<?xml version="1.0" encoding="utf-8"?>
<Configuration>
<Powerflow>
<networkConfiguration>IEEE14.raw</networkConfiguration>
<LinearSolver>
<PETScPrefix>nrs</PETScPrefix>
<PETScOptions>
-ksp_atol 1.0e-08
-ksp_rtol 1.0e-12
-ksp_monitor
-ksp_max_it 50
-ksp_view
</PETScOptions>
</LinearSolver>
</Powerflow>
</Configuration>

## Slide 80: Using the Configuration Module
// Using example input file from previous slide. Note that
// “open” is a collective operation, all others are local
Configuration *config = Configuration::configuration();
config->open(“input.xml”,MPI_COMM_WORLD);
// This returns “IEEE14.raw” in variable filename
std::string filename;
config.get(“Configuration.Powerflow.networkConfiguration”,
&filename);
// This also returns “IEEE14.raw” in variable filename
Cursor *cursor = config->getCursor(“Configuration.Powerflow”);
cursor->get(“networkConfiguration”,&filename);

## Slide 81: Serial IO
Works in conjunction with the writeSerial operation in the BaseComponent class
Designed to send output to standard out from buses and/or branches
11 0.942 -16.250 - - - -
12 0.943 -16.176 - - 16.70 1.70
13 0.926 -15.878 - - 16.10 1.60
21 0.964 -12.162 - - 196.20 19.60
23 0.964 -12.162 - - 0.10 0.10
31 0.967 -10.454 - - 79.20 7.90
32 0.967 -10.454 - - 79.20 7.90
41 0.978 -11.654 - - 106.70 10.70
43 0.978 -11.688 - - 5.60 0.60
51 0.937 -16.934 - - 63.70 6.40
52 0.940 -16.426 - - - -
61 0.909 -21.810 - - 23.20 2.30
62 0.905 -23.846 - - 23.40 2.30
75 0.923 -18.114 - - 21.30 2.10

## Slide 82: Serial IO Classes
// Write serial IO from buses. “len” is the maximum size
// string that is written. The string “signal” is passed
// to the writeSerial method in the BaseComponent class.
// The “write” method will trigger the writeSerial
// in the base and branch components, the “header” method
// is a convenience method for writing single strings
// from the head node
SerialBusIO(int len,
boost::shared_ptr<MyNetwork> network)
void write(char *signal)
void header(char *str)
// Write Serial IO from branches
SerialBranchIO(int len,
boost::shared_ptr<MyNetwork> network)
void write(char *signal)
void header(char *str)

## Slide 83: Using Serial IO
SerialBusIO busIO(256,network);
busIO.header(” Bus Voltage Generation Load\n”);
busIO.header(” # Mag(pu) Ang(deg) P (MW) Q (MVAr) P (MW) Q (MVAr)\n”);
busIO.header(” -------------------------------------------------------------------\n”);
busIO.write();
Use code fragment
to produce
Bus Voltage Generation Load
# Mag(pu) Ang(deg) P (MW) Q (MVAr) P (MW) Q (MVAr)
-------------------------------------------------------------------
11 0.942 -16.250 - - - -
12 0.943 -16.176 - - 16.70 1.70
13 0.926 -15.878 - - 16.10 1.60
21 0.964 -12.162 - - 196.20 19.60
23 0.964 -12.162 - - 0.10 0.10
31 0.967 -10.454 - - 79.20 7.90
32 0.967 -10.454 - - 79.20 7.90
41 0.978 -11.654 - - 106.70 10.70
These lines are produced from the serialWrite method in BaseComponentClass

## Slide 84: serialWrite method
bool gridpack::myapp::MyBus::serialWrite(char *string,
const char* signal){
sprintf(string,” %4d%7.3f%12.3f”,getOriginalIndex(),
p_volt, p_angle);
int len = strlen(string)
char *ptr = string + strlen
if (p_generator) {
sprintf(ptr,” %f12.3 %f12.3”,p_gen_p, p_gen_q);
} else {
sprintf(ptr,” - -”);
}
len = strlen(ptr);
ptr += len;
if (p_load) {
sprintf(ptr,” %f12.3 %f12.3\n”,p_load_p, p_load_q);
} else {
sprintf(ptr,” - -\n”);
}
}

## Slide 85: Directing Serial IO to Files
Use open and close methods to redirect output from standard out to a file
Same serial IO objects can be used to create multiple files
// Open file with name filename and direct all
// subsequent output to file
void open(const char *filename)
// Close file and redirect output back to standard
// out
void close(void)

## Slide 86: Powerflow Application Example
Create elements of Y-matrix and solve powerflow equations using a Newton-Raphson procedure.
  Powerflow components: set network parameters and evaluate matrix and vector elements
  Powerflow factory: coordinate higher level functions over the whole network
  Powerflow application: control program flow and implement higher level solver routine

## Slide 87
January 22, 2014
Configuration File
Topology File
Configure Module
Import Network
File
Name
Topology and parameters from network file
Network Object
Instantiate components
Network is ready for computation
Partition
Vector Map
Matrix Map
PQ
Jacobian
Nonlinear Solver
Solution
Factory
Output
Standard Output

## Slide 88: Powerflow Components
Create two new classes to represent buses and branches, PFBus and PFBranch
  These classes inherit from BaseBusComponent and BaseBranchComponent
  Create load methods in to initialize components from network configuration file parameters
  Implement routines to evaluate elements of Y-matrix on both bus and branches
  Implement functions in MatVecInterface to create Y-matrix, Jacobian matrix and right-hand-side (PQ) vector
  Set up buffers for data exchanges between processors
  Implement serialWrite method to create output

## Slide 89: PFBus::load
void gridpack::powerflow::PFBus::load(
const boost::shared_ptr<gridpack::component
::DataCollection> &data)
{
data->getValue(CASE_SBASE, &p_sbase);
:
int itype; data->getValue(BUS_TYPE, &itype);
if (itype == 3) {
setReferenceBus(true);
} elseif (…){…}
bool lgen;
int i, ngen, gstatus;
double pg, qg;
if (data->getValue(GENERATOR_NUMBER, &ngen)) {
for (i=0; i<ngen; i++) {
lgen = true;
lgen = lgen && data->getValue(GENERATOR_PG, &pg,i);
:
if (lgen) {
p_pg.push_back(pg);
:
}
}
}
}
Standard names defined in dictionary.hpp
“ngen” can be used to determine whether this bus has generators

## Slide 90: Evaluate Y-matrix parameters on buses
void gridpack::powerflow::PFBus::setYBus(void)
{
gridpack::ComplexType ret(0.0,0.0);
std::vector<boost::shared_ptr<BaseComponent> > branches;
getNeighborBranches(branches);
int size = branches.size();
int i;
for (i=0; i<size; i++) {
gridpack::powerflow::PFBranch *branch
= dynamic_cast<gridpack::powerflow::PFBranch*>
(branches[i].get());
ret -= branch->getAdmittance();
ret -= branch->getTransformer(this);
ret += branch->getShunt(this);
}
if (p_shunt) {
gridpack::ComplexType shunt(p_shunt_gs,p_shunt_bs);
ret += shunt;
}
p_ybusr = real(ret);
p_ybusi = imag(ret);
}
Functions defined on branches
Need to loop over branches attached to bus to evaluate bus contributions to Y-matrix
Y-matrix components assigned to internal variables
Loop over branches

## Slide 91: Diagonal Y-matrix contribution

## Slide 92: Evaluate Y-matrix parameters on branches
void gridpack::powerflow::PFBranch::setYBus(void)
{
gridpack::ComplexType ret(p_resistance,p_reactance);
ret = -1.0/ret;
gridpack::ComplexType a(cos(p_phase_shift),sin(p_phase_shift));
a = p_tap_ratio*a;
if (p_xform) {
p_ybusr_frwd = real(ret/conj(a));
p_ybusi_frwd = imag(ret/conj(a));
p_ybusr_rvrs = real(ret/a);
p_ybusi_rvrs = imag(ret/a);
} else {
p_ybusr_frwd = real(ret);
p_ybusi_frwd = imag(ret);
p_ybusr_rvrs = real(ret);
p_ybusi_rvrs = imag(ret);
}
gridpack::powerflow::PFBus *bus1 =
dynamic_cast<gridpack::powerflow::PFBus*>(getBus1().get());
gridpack::powerflow::PFBus *bus2 =
dynamic_cast<gridpack::powerflow::PFBus*>(getBus2().get());
p_theta = (bus1->getPhase() - bus2->getPhase());
}
Functions defined on buses
Evaluating contributions for
Yij and Yji

## Slide 93: PFBus::matrixDiagSize
bool gridpack::powerflow::PFBus::matrixDiagSize(int *isize,
int *jsize) const
{
if (p_mode == Jacobian) {
*isize = 2;
*jsize = 2;
return true;
} else if (p_mode == YBus) {
*isize = 1;
*jsize = 1;
return true;
}
}
The Y-matrix is built as a complex valued matrix, the Jacobian is written as a real-valued matrix, hence the 2x2 blocks instead of 1x1 blocks

## Slide 94: PFBus::matrixDiagValues
bool gridpack::powerflow::PFBus::matrixDiagValues(ComplexType *values)
{
if (p_mode == YBus) {
gridpack::ComplexType ret(p_ybusr,p_ybusi);
values[0] = ret;
return true;
} else if (p_mode == Jacobian) {
if (!getReferenceBus()) {
values[0] = -p_Qinj - p_ybusi * p_v *p_v;
values[1] = p_Pinj - p_ybusr * p_v *p_v;
values[2] = p_Pinj / p_v + p_ybusr * p_v;
values[3] = p_Qinj / p_v - p_ybusi * p_v;
if (p_isPV) {
values[1] = 0.0;
values[2] = 0.0;
values[3] = 1.0;
}
return true;
} else {
values[0] = 1.0;
values[1] = 0.0;
values[2] = 0.0;
values[3] = 1.0;
return true;
}
}
}
Note different return values depending on properties of bus

## Slide 95: PFBranch::matrixForwardValues
bool gridpack::powerflow::PFBranch::matrixForwardValues(
ComplexType *values)
{
if (p_mode == Jacobian) {
gridpack::powerflow::PFBus *bus1
= dynamic_cast<gridpack::powerflow::PFBus*>(getBus1().get());
:
bool ok = !bus1->getReferenceBus();
ok = ok && !bus2->getReferenceBus();
if (ok) {
double cs = cos(p_theta);
double sn = sin(p_theta);
values[0] = (p_ybusr_frwd*sn - p_ybusi_frwd*cs);
values[1] = (p_ybusr_frwd*cs + p_ybusi_frwd*sn);
values[2] = (p_ybusr_frwd*cs + p_ybusi_frwd*sn);
values[3] = (p_ybusr_frwd*sn - p_ybusi_frwd*cs);
:
bool bus1PV = bus1->isPV();
bool bus2PV = bus2->isPV();
if (bus1PV & bus2PV) {
:
}
return true;
} else {
return false;
}
} else if (p_mode == YBus) {
values[0] = gridpack::ComplexType(p_ybusr_frwd,p_ybusi_frwd);
return true;
}
For the reverse values function, use –p_theta instead of p_theta
Don’t contribute anything to the matrix if one end of the branch is attached to the reference bus

## Slide 96: Mapping Vectors
The MatVecInterface functions vectorSize and vectorValues work in a similar way to the matrix functions except that all data structures are 1D. The vector functions are only implemented on buses
The setValues function can be used to move values in a vector back onto buses. This is often done for the solution vector.
void gridpack::powerflow::PFBus::setValues(
gridpack::ComplexType *values)
{
p_a -= real(values[0]);
p_v -= real(values[1]);
*p_vAng_ptr = p_a;
*p_vMag_ptr = p_v;
}
Use values in the solution vector to modify internal bus variables

## Slide 97: Set up buffers for ghost bus and/or branch exchanges
int gridpack::powerflow::PFBus::getXCBufSize(void)
{
return 2*sizeof(double);
}
void gridpack::powerflow::PFBus::setXCBuf(void *buf)
{
p_vAng_ptr = static_cast<double*>(buf);
p_vMag_ptr = p_vAng_ptr+1;
*p_vAng_ptr = p_a;
*p_vMag_ptr = p_v;
}
Specify maximum amount of data to be exchanged
Assign slots in the allocated buffer to internal variables and initialize exchange variables
Note: all buses exchange the same amount of data, all branches exchange the same amount of data. Not all of the exchanged data needs to be used by any one particular bus or branch.

## Slide 98: Setting the Mode Variable
Both bus and branch components should define an enumerated type that defines the mode. Modes in powerflow app include
enum PFMode{YBus, Jacobian, RHS}
The bus and branch classes should define a simple modifier that sets the mode variable. Some other actions can also be taken when the mode is set
void gridpack::powerflow::PFBus::setMode(int mode)
{
p_mode = mode;
}

## Slide 99: Creating an Application Network
Once the application bus and branch classes are defined, it is possible to declare a typedef for the application network. This is not strictly necessary, but it is usually a tremendous convenience
typedef gridpack::network::BaseNetwork<PFBus, PFBranch > PFNetwork;

## Slide 100: Powerflow Factory
Create a powerflow factory class by subclassing the BaseFactory class
Inherit base class methods such as setComponents and setExchange
class PFFactory
: public gridpack::factory::BaseFactory<PFNetwork> {
:
:
};

## Slide 101: New Factory Methods
A typical application-specific factory method would be the setYBus function
Loop over buses and invoke bus method, then loop over branches and invoke branch method
void gridpack::powerflow::PFFactory::setYBus(void)
{
int numBus = p_network->numBuses();
int numBranch = p_network->numBranches();
int i;
for (i=0; i<numBus; i++) {
dynamic_cast<PFBus*>(p_network->getBus(i).get())->setYBus();
}
for (i=0; i<numBranch; i++) {
dynamic_cast<PFBranch*>(p_network->getBranch(i).get())->setYBus();
}
}

## Slide 102: Powerflow Main Application
A small “main” program calls the powerflow application class and executes the simulation. This separates some initialization from the rest of the application and guarantees that objects exit cleanly
An application class controls overall program flow and implements the solution algorithm
  Read in network from external configuration file
  Initialize network and set up matrices and vectors
  Implement solution method
  Export results to standard out or to files

## Slide 103: Powerflow “main” Program
Initialize communication libraries (MPI and GA) and math component. Initializing math component invokes initialization routines in underlying math libraries.
Execute application
main(int argc, char **argv)
{
int ierr = MPI_Init(&argc, &argv);
gridpack::math::Initialize();
GA_Initialize();
int stack = 200000, heap = 200000;
MA_init(C_DBL, stack, heap);
gridpack::powerflow::PFApp app;
app.execute();
GA_Terminate();
gridpack::math::Finalize();
ierr = MPI_Finalize();
}

## Slide 104: Powerflow Execution: Setting Up Network
gridpack::parallel::Communicator world;
boost::shared_ptr<PFNetwork> network(new PFNetwork(world));
gridpack::utility::Configuration *config
= gridpack::utility::Configuration::configuration();
config->open("input.xml",world);
gridpack::utility::Configuration::Cursor *cursor;
cursor = config->getCursor("Configuration.Powerflow");
std::string filename = cursor->get("networkConfiguration",
"No network configuration specified");
gridpack::parser::PTI23_parser<PFNetwork> parser(network);
parser.parse(filename.c_str());
network->partition();
Create network
Open input file
Read in name of network configuration file
Read in network
Partition network between processors

## Slide 105: Powerflow Application: Using Factory to Complete Network Initialization
gridpack::powerflow::PFFactory factory(network);
factory.load();
factory.setComponents();
factory.setExchange();
network->initBusUpdate();
factory.setYBus();
Move data from DataCollection objects to bus and branch objects
Set internal indices and buffers
Set up data exchanges between buses
Evaluate Y-matrix components

## Slide 106: Powerflow Application: Creating Mappers and Generating Matrices and Vectors
factory.setMode(YBus);
gridpack::mapper::FullMatrixMap<PFNetwork> mMap(network);
boost::shared_ptr<gridpack::math::Matrix> Y = mMap.mapToMatrix();
factory.setSBus();
factory.setMode(RHS);
gridpack::mapper::BusVectorMap<PFNetwork> vMap(network);
boost::shared_ptr<gridpack::math::Vector> PQ = vMap.mapToVector();
factory.setMode(Jacobian);
gridpack::mapper::FullMatrixMap<PFNetwork> jMap(network);
boost::shared_ptr<gridpack::math::Matrix> J = jMap.mapToMatrix();
boost::shared_ptr<gridpack::math::Vector> X(PQ->clone());
Y-matrix
Right hand side vector
Jacobian
Solution vector

## Slide 107: Powerflow Application: Initialize Newton-Raphson Loop
double tolerance = 1.0e-6;
int max_iteration = 100;
ComplexType tol;
gridpack::math::LinearSolver solver(*J);
solver.configure(cursor);
int iter = 0;
X->zero();
solver.solve(*PQ, *X);
tol = PQ->normInfinity();
Set parameters
Set up linear solver an set solver parameters from input file
Solve linear equation and evaluate norm of solution vector

## Slide 108: Powerflow Application: execute Newton-Raphson Iterations
while (real(tol) > tolerance && iter < max_iteration) {
factory.setMode(RHS);
vMap.mapToBus(X);
network->updateBuses();
vMap.mapToVector(PQ);
factory.setMode(Jacobian);
jMap.mapToMatrix(J);
X->zero();
solver.solve(*PQ, *X);
tol = PQ->normInfinity();
iter++;
}
factory.setMode(RHS);
vMap.mapToBus(X)
Move solution vector back to buses and exchange data between buses
Create new Jacobian and right hand side vector from updated bus values
Resolve equations
Push final result back onto buses

## Slide 109: Powerflow Application: Export Results to Standard Output
gridpack::serial_io::SerialBusIO<PFNetwork> busIO(128,network);
busIO.header("\n Bus Voltages and Phase Angles\n");
busIO.header("\n Bus Number Phase Angle");
busIO.header(" Voltage Magnitude\n");
busIO.write();
Bus Voltages and Phase Angles
Bus Number Phase Angle Voltage Magnitude
1 0.000000 1.060000
2 -4.982589 1.045000
3 -12.725100 1.010000
4 -10.312901 1.017671
5 -8.773854 1.019514
6 -14.220946 1.070000
7 -13.359627 1.061520
8 -13.359627 1.090000
9 -14.938521 1.055932
10 -15.097288 1.050985
11 -14.790622 1.056907
12 -15.075585 1.055189
13 -15.156276 1.050382
14 -16.033645 1.035530
Write header
Write data from buses