## Slide 1: GridPACK™ Framework for Developing Power Grid Applications for HPC Platforms
Bruce Palmer, Bill Perkins, Kevin Glass, Yousu Chen, Shuangshuang Jin, Ruisheng Diao, Mark Rice, David Callahan, Steve Elbert, Henry Huang

## Slide 2: Objective
Develop a framework to support the rapid development of power grid software applications on HPC platforms
Extend the penetration of HPC in power grid modeling
Provide high level abstractions for often used motifs in power grid applications
Reduce the amount of explicit communication that must be handled by developers
Allow power grid application developers to focus on physics and algorithms and not on parallel computing

## Slide 3: Approach
Develop software modules that encapsulate commonly used functionality in HPC power grid applications
Setup and distribution of power grid networks
Input/Output
Mapping from grid to distributed matrices
Parallel solvers
Incorporate advanced parallel libraries whenever possible
  PETSc, ParMETIS

## Slide 4
Core Data Objects
Power Grid Network and Fields
Matrices and Vectors
Network Components
Neighbor Lists
Matrix Elements
Application Factory
Solver
Math Module
PETSc
Mapper
Network Module
Ghost Exchanges
Partitioning
Matrix and Vector Module
PETSc
Applications
Import Module
PTI Formats
Dictionary
Export Module
Serial IO
PTI Formats
GridPACK™ Framework
Configure Module
XML
GridPACK™ Software Stack
Utilities
Errors
Logging
Profiling

## Slide 5: Application Flow Diagram
Configuration File
Topology File
Configure Module
Import Network
Network Module
Partition
Network Object
Solver Module
Mapper
Math Module
Export Network
Output File
Factory
Network Object
Network topology, simple fields
Network topology, network components
Network Component

## Slide 6: Modules
Network: Manages the topology, neighbor lists, parallel distribution and indexing. Acts as a container for bus and branch components
Bus and Branch components: define the behavior and properties of buses and branches in network. These components also define the matrices that can be generated as part of the simulation
Factory: Manages interactions between network and the components

## Slide 7: Instantiate a Network
#include “gridpack/network/BaseNetwork.hpp”
#include “gridpack/applications/myapp/mycomponents.hpp”
typedef gridpack::network::BaseNetwork
<gridpack::myapp::MyBus,
gridpack::myapp::MyBranch> MyNetwork;
boost::shared_ptr<MyNetwork> network(new MyNetwork);
// Create a network object that has the application-specific
// bus and branch models associated with it. The network will
// also have DataCollection objects on each bus and branch.
// At this point, the network is just a container and has no
// topology or datak

## Slide 8: Create Network from External File
#include “gridpack/parser/ParserPTI.hpp”
:
gridpack::parser::PTI23_parser<MyNetwork> parser(network);
parser.parse(“location_of_PTI_file”);
// The network topology now exists and the data
// collection objects on each bus and branch are filled
// with parameters from the PTI file. The network is
// NOT, however, distributed in an optimal way at this
// point. Also, no ghost buses or ghost branches have
// been added to the network yet, so most calculations
// not possible

## Slide 9: Network Topology
Bus
Branch

## Slide 10: Network Data
Data Collection Objects on Buses
Data Collection Objects on Branches

## Slide 11: Network Components
Uninitialized Bus Component
Uninitialized Branch Component

## Slide 12: Partition Network
// Invoke the partition function
network->partition();
// Network has been properly distributed among
// processors, ghost buses and ghost branches have been
// added to the network, and global indices have been
// set. Local neighbor lists and indices for the ends
// branches have also been set. Network is almost ready
// for calculations

## Slide 13: Partitioning the Network
Process 0
Process 1

## Slide 14: Process 0 Partition
Process 0
Ghost Buses and Branches

## Slide 15: Process 1 Partition
Process 1
Ghost Buses and Branches

## Slide 16: Base Network Class
// Return number of buses and branches on this process
// (including ghost buses and branches)
int numBuses(void);
int numBranches(void);
// Get local index of reference bus (return -1 if
// reference bus is not on this process)
int getReferenceBus(void) const;
// Return true if bus or branch is local to the process,
// return false for ghost buses and branches
bool getActiveBus(int idx);
bool getActiveBranch(int idx);
// Return pointer to bus or branch object corresponding
// to local index idx
boost::shared_ptr<MyBus> getBus(int idx);
boost::shared_ptr<MyBranch> getBranch(int idx);

## Slide 17: Base Network Class
// Return pointer to DataCollection objects associated
// with bus or branch at local index idx
boost::shared_ptr<gridpack::component::DataCollection>
getBusData(int idx);
boost::shared_ptr<gridpack::component::DataCollection>
getBranchData(int idx);
// Remove all ghost buses and branches from the network
void clean(void);
// Set up data structures for exchanges to ghosts buses
// and branches
void initBusUpdate(void);
void initBranchUpdate(void);
// Send data to ghost buses and branches
void updateBuses(void);
void updateBranches(void)

## Slide 18: Factories
Factories are designed to set up the system so that it can be used in calculations. They guarantee the all bus and branch objects are in the correct state for generating the correct matrices and vectors needed for solving the problem
A primary motif in factory methods is that they loop over all bus and branch objects and invoke methods on them that set a particular state

## Slide 19: Base Factory Class
// Set up lists of pointers in each component to
// neighbors of all buses and branches in the
// network
virtual void setComponents(void);
// The “load” operation takes all the data from the
// data collection objects and moves them into the
// corresponding bus and branch components using the
// load functions that have been defined in the
// individual bus and branch classes
virtual void load(void);

## Slide 20: Base Factory Class
// Set up internal buffers so that data exchanges to
// fill up ghost branches and ghost buffers will work.
// To exchange data, users need to put the data in the
// component’s exchange buffer and then invoke a bus
// or branch ghost exchange in the network
virtual void setExchange(void);
// Invoke the setMode method on all bus and branch
// components in the network. The mode can be used to
// control the behavior of the network components at // different stages of the calculation
virtual void setMode(int mode);

## Slide 21: Example of a Factory Method
/**
* Generic method that invokes the "load" method
* on all branches and buses to move data from
* the DataCollection objects on the network into the
* corresponding buses and branches
*/
void gridpack::factory::BaseFactory<MyNetwork>::load(void)
{
int numBus = p_network->numBuses();
int numBranch = p_network->numBranches();
int i;
// Invoke load method on all bus objects
for (i=0; i<numBus; i++) {
p_network->getBus(i)->load(p_network->getBusData(i));
}
// Invoke load method on all branch objects
for (i=0; i<numBranch; i++) {
p_network->getBranch(i)->load(p_network->getBranchData(i));
}
}

## Slide 22: Initialize Components
Use data in Data Collections to initialize bus and branch components via the load method

## Slide 23: Create a New Factory
Class MyFactory
: public gridpack::factory::BaseFactory<MyNetwork> {
MyFactory(NetworkPtr network);
~MyFactory();
MyFactoryMethod1(…);
MyFactoryMethod2(…);
:
:
}

## Slide 24: Initialize Components
#include “gridpack/applications/myapp/MyFactory.hpp
:
gridpack::myapp::MyFactory factory(network);
// Initialize components with data from DataCollection
// objects
factory.load();
// Set up internal indices used by mappers to create
// matrices and vectors and set pointers for
// neighboring buses and branches
factory.setComponents();
// Set up buffers for ghost exchanges
factory.setExchange();

## Slide 25: Components
All components are derived from the MatVecInterface class and the BaseComponent class
Bus components are derived from the BaseBusComponent class
Branch components are derived from the BaseBranchComponent class

## Slide 26: Component Class Hierarchy
MatVecInterface
BaseComponent
BaseBusComponent
BaseBranchComponent
AppBusComponent
AppBranchComponent

## Slide 27: The MatVecInterface
Designed to allow the GridPACK™ framework to generate matrices and vectors from individual bus and branch components
Buses and branches are responsible for describing their individual contribution to matrices and vectors
Buses and branches are NOT responsible for determining location in matrix or vector and are NOT responsible for distributing matrices or vectors

## Slide 28: Diagonal MatVecInterface
// Return the size of matrix block on the diagonal.
// Usually implemented on bus components. This function
// returns false if the component does not contribute
// anything to the matrix
virtual bool matrixDiagSize(int *isize,
int *jsize) const
// Return the values of the block in row-major order.
// Return false if component does not contribute to matrix
virtual bool matrixDiagValues(ComplexType *values)

## Slide 29: Off-diagonal MatVecInterface
// Return the size an off-diagonal matrix block
// contributed by the component. This function returns
// false if no values are contributed by component. These
// functions are usually implemented on branches. The
// Forward function is called for an ij pair when i
// corresponds to the “from” bus defining a branch.
// The Reverse function is called when i corresponds
// to the “to” bus
virtual bool matrixForwardSize(int *isize,
int *jsize) const
virtual bool matrixReverseSize(int *isize,
int *jsize) const
// Return the and values of off-diagonal matrix block.
// Values are in row-major order.
virtual bool matrixForwardValues(ComplexType *values)
virtual bool matrixReverseValues(ComplexType *values)

## Slide 30: Vector MatVecInterface
// Return the block size of component contribution to
// a vector. Return false if a component does not
// contribute to vector
virtual bool vectorSize(int *isize) const
// Return the values of the vector block contributed
// by component
virtual bool vectorValues(ComplexType *values)

## Slide 31: BaseComponent
This class provides a few methods that are needed by all network components (bus or branch)
Provides methods for moving data from DataCollection objects to components and sets up buffers used for ghost bus and ghost branch exchanges
Provides a mechanism for changing component behavior so that different matrices can be extracted from components during different phases of the calculation

## Slide 32: BaseComponent
// Load data from DataCollection object into component
virtual void load(const shared_ptr<DataCollection> &data)
// Return the size of the buffer needed for data exchanges
// Note that all bus components must return the same value
// for this function and all branch components must return
// the same value
virtual int getXCBufSize(void)
// Write out a single string describing current state of
// the component. The character string “signal” can be used
// to control the behavior of the component. Return false
// if no string is being returned. This functionality is
// used in the serialIO module
virtual bool serialWrite(char *string, char *signal)

## Slide 33: BaseComponent::setMode
Each bus and branch component should have an internal mode variable corresponding to an enumerated type
Different values of the mode variable can generate different behaviors. For example, the network components in a powerflow application must be able to generate both the Y-matrix and the Jacobian for a powerflow calculation
  If the mode is set to “YBus”, the MatVecInterface functions return values appropriate for creating the Y-matrix
  If the mode is set to “Jacobin”, the MatVecInterface functions return values appropriate for generating the Jacobian matrix used in the powerflow equations
void setMode(int mode)

## Slide 34: BaseBusComponent
Provides methods that are needed by all bus component implementations
Sets up lists of branches that are attached to the bus and buses that are attached via a single branch
Keeps track of the reference bus

## Slide 35: BaseBusComponent
// Get pointers to branches that are connected to bus
void getNeighborBranches(vector<shared_ptr
<BaseComponent> > &nghbrs) const
// Get pointers to buses that are connected to bus via
// a single branch
void getNeighborBuses(vector<shared_ptr
<BaseComponent> > &nghbrs) const
// If bus is reference bus, set status to true
void setReferenceBus(bool status)
// Return true if this bus is reference bus
bool getReferenceBus(void) const

## Slide 36: BaseBranchComponent
Provides methods that are needed by all branch component implementations
Keeps track of the buses at each end of the branch and makes these available to the application

## Slide 37: BaseBranchComponent
// Get pointers to buses at either end of the branch.
// Bus 1 refers to the “from” bus and bus 2 refers to
// the “to” bus
shared_ptr<BaseComponent> getBus1(void) const
shared_ptr<BaseComponent> getBus2(void) const

## Slide 38: DataCollection Objects
Every bus and branch in the network has an associated DataCollection object
The DataCollection object is a container for key-value pairs of parameters associated with a particular bus or branch
Different buses and branches can contain different numbers of key-value pairs and different types of key-value pairs
If a bus or branch has a list of values associated with the same key, then these can be indexed
Key-value pairs are usually added to the DataCollection objects when the network is read in from a network configuration file

## Slide 39: DataCollection Accessors
bool getValue(char *name, int *value);
bool getValue(char *name, long *value);
bool getValue(char *name, bool *value);
bool getValue(char *name, std::string *value);
bool getValue(char *name, float *value);
bool getValue(char *name, double *value);
bool getValue(char *name, gridpack::ComplexType *value);
bool getValue(char *name, int *value, int idx);
bool getValue(char *name, long *value, int idx);
bool getValue(char *name, bool *value, int idx);
bool getValue(char *name, std::string *value, int idx);
bool getValue(char *name, float *value, int idx);
bool getValue(char *name, double *value, int idx);
bool getValue(char *name, gridpack::ComplexType *value,
int idx);

## Slide 40: Mapper
Provide a flexible framework for constructing matrices and vectors representing power grid equations
Hide the index transformations and partitioning required to create distributed matrices and vectors from application developers
Developers can focus on the contributions to matrices and vectors coming from individual network elements

## Slide 41: Mapper
1
2
3
4
5
6
7
8
12
11
10
9

## Slide 42: Matrix Contributions from Components
1
2
3
4
5
6
7
8
12
11
10
9
No matrix contribution
No matrix contribution
No matrix contribution

## Slide 43: Distribute Component Contributions and Eliminate Gaps

## Slide 44: Matrix Mapper Interface
// Instantiate a new mapper that creates a matrix from
// bus and branch components on the network
void FullMatrixMap(shared_ptr<MyNetwork> network);
// Create a matrix from the network
shared_ptr<Matrix> mapToMatrix(void);
// Reset matrix based on current network values
void mapToMatrix(shared_ptr<Matrix> &M);

## Slide 45: Vector Mapper Interface
// Instantiate a new mapper that creates a vector from
// bus components on the network
void BusVectorMap(shared_ptr<MyNetwork> network);
// Create a vector from the network
shared_ptr<Vector> mapToVector(void);
// Reset vector based on current network values
void mapToVector(shared_ptr<Matrix> &M);
// Push current values in vector back into buses
void mapToBus(Vector &vector);

## Slide 46: Mapper Behavior
The matrix or vector that is produced by a mapper is controlled by
  The functions that are implemented in the MatVecInterface by the application developer
  The current value of the mode variable. If the application needs to create different matrices or vectors based on different modes, then separate mappers should be created for each mode
  When calling any of the mapper functions, the mode should always be set to the same value as the mode that was in place when the mapper was created

## Slide 47: Algebraic Operations
The math module is a wrapper on top of a parallel solver library. It supports
  Distributed sparse and dense matrices and distributed vectors
  Basic manipulations of matrices and vectors, e.g. matrix additions, matrix-vector multiplication, scaling of matrices, creation of identity matrix, etc.
  Linear solvers that support different algorithms and preconditioners for solving the matrix equation Ax=b
  Nonlinear solvers

## Slide 48: Math Library
// Initialize math library. Call any initialization
// routines that are necessary and read in any
// configuration files. Currently, PETSc options are
// listed in a gridpack.petscrc file. This is were
// preconditioners and other PETSc configuration
// parameters are specified.
extern void Initialize(void);
// Is math library initialized?
extern bool Initialized(void);
// Shut down math library
extern void Finalize();

## Slide 49: Vector Class
// Specify parallel configuration and local contribution
// to vector in constructor
Vector(const parallel::Communicator &comm,
const int &local_length);
// Accessors for vector properties
int size(void) const;
int localSize(void) const;
void localIndexRange(int &lo, int &hi) const;

## Slide 50: Vector Class
// Set vector elements
void setElement(const int &i, const ComplexType &x);
void setElements(const int &n, const int *i,
const ComplexType *x);
// Access matrix elements
void getElement(const int &i, ComplexType &x) const;
void getElements(const int &n, const int *i,
ComplexType *x) const;
// Indicate vector is ready to use
void ready(void);

## Slide 51: Basic Vector Operations
// Basic operations that can be performed on vectors
void zero(void);
void fill(const ComplexType &v);
ComplexType norm1(void) const;
ComplexType norm2(void) const;
void scale(const ComplexType &x);
void add(const Vector &x, const ComplexType &scale = 1.0);
void equate(const Vector &x);
void reciprocal(void);

## Slide 52: Matrix Class
// Specify dimensions and storage format of matrix in
// constructor. Also the parallel configuration
Matrix(const parallel::Communicator &dist,
const int &local_rows,
const int &cols,
const StorageType &storage_type=Sparse);
// Accessors for matrix properties
int rows(void) const;
int localRows(void) const;
int cols(void) const;

## Slide 53: Matrix Class
// Set matrix elements
void setElement(const int &i, const int &j,
const ComplexType &x);
void setElements(const int &n, const int *i,
const int *j, const ComplexType *x);
// Access matrix elements
void getElement(const int &i, const int &j,
ComplexType &x) const;
Void getElements(const int &n, const int *i,
const int *j, ComplexType *x) const;
// Indicate matrix is ready
void ready(void);

## Slide 54: Basic Matrix Operations
// Basic operations that can be performed on matrices
void equate(const Matrix &A);
void scale(const ComplexType &x);
void multiplyDiagonal(const Vector &x);
void add(const Matrix &A);
void identity(void);
void zero(void);
// Matrix-Vector operations
extern Matrix *add(const &A, const &B);
extern Matrix *transpose(const Matrix &A);
extern Vector *column(const Matrix &A, const int &cidx);
extern Vector *diagonal(const Matrix &A);
extern Matrix *multiply(const Matrix &A, const Matrix &B);
extern Vector *multiply(const Matrix &A, const Vector &x);

## Slide 55: Linear Solver
// Solve equation using and instance of a LinearSolver
LinearSolver(const Matrix &A);
void solve(const Vector &b, Vector &x) const;

## Slide 56: Configure
Configure is designed to take user input, in the form of an XML-based input file, and transfer that information to any parts of the code that might need it. Configure is designed to handle relatively limited amounts of data, it is not designed for handling large data objects like the network. Examples of user input include
  Location of network configuration file
  Type of solvers to use
  Solution parameters such as convergence tolerance, maximum number of iterations, etc.
  Control parameters for different types of data output

## Slide 57: Configuration Module
// Access common instance of configuration module,
// shared across all modules
static Configuration* configuration()
// Open external configuration file
bool open(std::string file, MPI_comm comm)
typedef Configuration Cursor
// Set the “cursor” in the Configuration object so
// that it only looks at key-value pairs within the
// block delimited by “key”
Cursor* getCursor(std::string key)

## Slide 58: Configuration Accessors
// Return default value if no value for that key is
// set in input file
bool get(std::string, bool default_value)
int get(std::string, int default_value)
double get(std::string, double default_value)
std::string get(std::string,
std::string default_value)
std::vector<double> get(std::string,
std::vector<double> default_value)
// Return value for key, value of function is
// false if no value found
bool get(std::string, bool *value)
bool get(std::string, int *value)
bool get(std::string, double *value)
bool get(std::string, std::string *value)
bool get(std::string, std::vector<double> *value)

## Slide 59: Input File example
<?xml version="1.0" encoding="utf-8"?>
<Configuration>
<Powerflow>
<networkConfiguration>IEEE14.raw</networkConfiguration>
<LinearSolver>
<PETScPrefix>nrs</PETScPrefix>
<PETScOptions>
-ksp_atol 1.0e-08
-ksp_rtol 1.0e-12
-ksp_monitor
-ksp_max_it 50
-ksp_view
</PETScOptions>
</LinearSolver>
</Powerflow>
</Configuration>

## Slide 60: Using the Configuration Module
// Using example input file from previous slide
Configuration *config = Configuration::configuration();
config->open(“input.xml”,MPI_COMM_WORLD);
// This returns “IEEE14.raw” in variable filename
std::string filename;
config.get(“Configuration.Powerflow.networkConfiguration”,
&filename);
// This also returns “IEEE14.raw” in variable filename
Cursor *cursor = config->getCursor(“Configuration.Powerflow”);
cursor->get(“networkConfiguration”,&filename);

## Slide 61: Serial IO
Works in conjunction with the writeSerial operation in the BaseComponent class
Designed to send output to standard out from buses and/or branches
11 0.942 -16.250 - - - -
12 0.943 -16.176 - - 16.70 1.70
13 0.926 -15.878 - - 16.10 1.60
21 0.964 -12.162 - - 196.20 19.60
23 0.964 -12.162 - - 0.10 0.10
31 0.967 -10.454 - - 79.20 7.90
32 0.967 -10.454 - - 79.20 7.90
41 0.978 -11.654 - - 106.70 10.70
43 0.978 -11.688 - - 5.60 0.60
51 0.937 -16.934 - - 63.70 6.40
52 0.940 -16.426 - - - -
61 0.909 -21.810 - - 23.20 2.30
62 0.905 -23.846 - - 23.40 2.30
75 0.923 -18.114 - - 21.30 2.10

## Slide 62: Serial IO Classes
// Write serial IO from buses. “len” is the maximum size
// string that is written. The string “signal” is passed
// to the writeSerial method in the BaseComponent class.
// The “write” method will trigger the writeSerial
// in the base and branch components, the “header” method
// is a convenience method for writing single strings
// from the head node
SerialBusIO(int len,
boost::shared_ptr<MyNetwork> network)
void write(char *signal)
void header(char *str)
// Write Serial IO from branches
SerialBranchIO(int len,
boost::shared_ptr<MyNetwork> network)
void write(char *signal)
void header(char *str)

## Slide 63: Using Serial IO
SerialBusIO busIO(256,network);
busIO.header(” Bus Voltage Generation Load\n”);
busIO.header(” # Mag(pu) Ang(deg) P (MW) Q (MVAr) P (MW) Q (MVAr)\n”);
busIO.header(” -------------------------------------------------------------------\n”);
busIO.write();
Use code fragment
to produce
Bus Voltage Generation Load
# Mag(pu) Ang(deg) P (MW) Q (MVAr) P (MW) Q (MVAr)
-------------------------------------------------------------------
11 0.942 -16.250 - - - -
12 0.943 -16.176 - - 16.70 1.70
13 0.926 -15.878 - - 16.10 1.60
21 0.964 -12.162 - - 196.20 19.60
23 0.964 -12.162 - - 0.10 0.10
31 0.967 -10.454 - - 79.20 7.90
32 0.967 -10.454 - - 79.20 7.90
41 0.978 -11.654 - - 106.70 10.70
These lines are produced from the writeSerial method in BaseComponentClass

## Slide 64: Powerflow Application Example
Create elements of Y-matrix and solve powerflow equations using a Newton-Raphson procedure.
  Powerflow components: set network parameters and evaluate matrix and vector elements
  Powerflow factory: coordinate higher level functions over the whole network
  Powerflow application: control program flow and implement higher level solver routine

## Slide 65
October 28, 2013
Configuration File
Topology File
Configure Module
Import Network
File
Name
Topology and parameters from network file
Network Object
Instantiate components
Network is ready for computation
Partition
Vector Map
Matrix Map
PQ
Jacobian
Nonlinear Solver
Solution
Factory
Output
Standard Output

## Slide 66: Powerflow Components
Create two new classes to represent buses and branches, PFBus and PFBranch
  These classes inherit from BaseBusComponent and BaseBranchComponent
Create load methods in to initialize components from network configuration file parameters
Implement routines to evaluate elements of Y-matrix on both bus and branches
Implement functions in MatVecInterface to create Y-matrix, Jacobian matrix and right-hand-side vector
Set up buffers for data exchanges between processors
Implement serialWrite method to create output

## Slide 67: PFBus::load
void gridpack::powerflow::PFBus::load(
const boost::shared_ptr<gridpack::component
::DataCollection> &data)
{
data->getValue(CASE_SBASE, &p_sbase);
:
int itype; data->getValue(BUS_TYPE, &itype);
if (itype == 3) {
setReferenceBus(true);
}
bool lgen;
int i, ngen, gstatus;
double pg, qg;
if (data->getValue(GENERATOR_NUMBER, &ngen)) {
for (i=0; i<ngen; i++) {
lgen = true;
lgen = lgen && data->getValue(GENERATOR_PG, &pg,i);
:
if (lgen) {
p_pg.push_back(pg);
:
}
}
}
}
Standard names defined in dictionary.hpp
This loop can be used to determine whether this bus has generators

## Slide 68: Evaluate Y-matrix parameters on buses
void gridpack::powerflow::PFBus::setYBus(void)
{
gridpack::ComplexType ret(0.0,0.0);
std::vector<boost::shared_ptr<BaseComponent> > branches;
getNeighborBranches(branches);
int size = branches.size();
int i;
for (i=0; i<size; i++) {
gridpack::powerflow::PFBranch *branch
= dynamic_cast<gridpack::powerflow::PFBranch*>
(branches[i].get());
ret -= branch->getAdmittance();
ret -= branch->getTransformer(this);
ret += branch->getShunt(this);
}
if (p_shunt) {
gridpack::ComplexType shunt(p_shunt_gs,p_shunt_bs);
ret += shunt;
}
p_ybusr = real(ret);
p_ybusi = imag(ret);
}
Functions defined on branches
Need to loop over branches attached to bus to evaluate bus contributions to Y-matrix

## Slide 69: Evaluate Y-matrix parameters on branches
void gridpack::powerflow::PFBranch::setYBus(void)
{
gridpack::ComplexType ret(p_resistance,p_reactance);
ret = -1.0/ret;
gridpack::ComplexType a(cos(p_phase_shift),sin(p_phase_shift));
a = p_tap_ratio*a;
if (p_xform) {
p_ybusr_frwd = real(ret/conj(a));
p_ybusi_frwd = imag(ret/conj(a));
p_ybusr_rvrs = real(ret/a);
p_ybusi_rvrs = imag(ret/a);
} else {
p_ybusr_frwd = real(ret);
p_ybusi_frwd = imag(ret);
p_ybusr_rvrs = real(ret);
p_ybusi_rvrs = imag(ret);
}
gridpack::powerflow::PFBus *bus1 =
dynamic_cast<gridpack::powerflow::PFBus*>(getBus1().get());
gridpack::powerflow::PFBus *bus2 =
dynamic_cast<gridpack::powerflow::PFBus*>(getBus2().get());
p_theta = (bus1->getPhase() - bus2->getPhase());
}
Functions defined on buses
Evaluating contributions for
Yij and Yji

## Slide 70: PFBus::matrixDiagSize
bool gridpack::powerflow::PFBus::matrixDiagSize(int *isize,
int *jsize) const
{
if (p_mode == Jacobian) {
*isize = 2;
*jsize = 2;
return true;
} else if (p_mode == YBus) {
*isize = 1;
*jsize = 1;
return true;
}
}
The Y-matrix is built as a complex valued matrix, the Jacobian is written as a real-valued matrix, hence the 2x2 blocks instead of 1x1 blocks

## Slide 71: PFBus::matrixDiagValues
bool gridpack::powerflow::PFBus::matrixDiagValues(ComplexType *values)
{
if (p_mode == YBus) {
gridpack::ComplexType ret(p_ybusr,p_ybusi);
values[0] = ret;
return true;
} else if (p_mode == Jacobian) {
if (!getReferenceBus()) {
values[0] = -p_Qinj - p_ybusi * p_v *p_v;
values[1] = p_Pinj - p_ybusr * p_v *p_v;
values[2] = p_Pinj / p_v + p_ybusr * p_v;
values[3] = p_Qinj / p_v - p_ybusi * p_v;
if (p_isPV) {
values[1] = 0.0;
values[2] = 0.0;
values[3] = 1.0;
}
return true;
} else {
values[0] = 1.0;
values[1] = 0.0;
values[2] = 0.0;
values[3] = 1.0;
return true;
}
}
}
Note different return values depending on properties of bus

## Slide 72: PFBranch::matrixForwardValues
bool gridpack::powerflow::PFBranch::matrixForwardValues(
ComplexType *values)
{
if (p_mode == Jacobian) {
gridpack::powerflow::PFBus *bus1
= dynamic_cast<gridpack::powerflow::PFBus*>(getBus1().get());
:
bool ok = !bus1->getReferenceBus();
ok = ok && !bus2->getReferenceBus();
if (ok) {
double cs = cos(p_theta);
double sn = sin(p_theta);
values[0] = (p_ybusr_frwd*sn - p_ybusi_frwd*cs);
values[1] = (p_ybusr_frwd*cs + p_ybusi_frwd*sn);
values[2] = (p_ybusr_frwd*cs + p_ybusi_frwd*sn);
values[3] = (p_ybusr_frwd*sn - p_ybusi_frwd*cs);
:
bool bus1PV = bus1->isPV();
bool bus2PV = bus2->isPV();
if (bus1PV & bus2PV) {
:
}
return true;
} else {
return false;
}
} else if (p_mode == YBus) {
values[0] = gridpack::ComplexType(p_ybusr_frwd,p_ybusi_frwd);
return true;
}
For the reverse values function, use –p_theta instead of p_theta
Don’t contribute anything to the matrix if one end of the branch is attached to the reference bus

## Slide 73: Creating Vectors
The MatVecInterface functions vectorSize and vectorValues work in a similar way to the matrix functions except that all data structures are 1D. The vector functions are only implemented on buses
The setValues function can be used to move values in a vector back onto buses. This is often done for the solution vector.
void gridpack::powerflow::PFBus::setValues(
gridpack::ComplexType *values)
{
p_a -= real(values[0]);
p_v -= real(values[1]);
*p_vAng_ptr = p_a;
*p_vMag_ptr = p_v;
}
Use values in the solution vector to modify internal bus variables

## Slide 74: Set up buffers for ghost bus and/or branch exchanges
int gridpack::powerflow::PFBus::getXCBufSize(void)
{
return 2*sizeof(double);
}
void gridpack::powerflow::PFBus::setXCBuf(void *buf)
{
p_vAng_ptr = static_cast<double*>(buf);
p_vMag_ptr = p_vAng_ptr+1;
*p_vAng_ptr = p_a;
*p_vMag_ptr = p_v;
}
Specify maximum amount of data to be exchanged
Assign slots in the allocated buffer to internal variables and initialize exchange variables
Note: all buses exchange the same amount of data, all branches exchange the same amount of data. Not all of the exchanged data needs to be used by any one particular bus or branch.

## Slide 75: Setting the Mode Variable
Both bus and branch components should define an enumerated type that defines the mode
The bus and branch classes should define a simple modifier that sets the mode variable. Some other actions can also be taken when the mode is set
void gridpack::powerflow::PFBus::setMode(int mode)
{
p_mode = mode;
}

## Slide 76: Creating an Application Network
Once the application bus and branch classes are defined, it is possible to declare a typedef for the application network. This is not strictly necessary, but it is usually a tremendous convenience
typedef gridpack::network::BaseNetwork<PFBus, PFBranch > PFNetwork;

## Slide 77: Powerflow Factory
Create a powerflow factory class by subclassing the BaseFactory class
Inherit base class methods such as setComponents and setExchange
class PFFactory
: public gridpack::factory::BaseFactory<PFNetwork> {
};

## Slide 78: New Factory Methods
A typical application-specific factory method would be the setYBus function
Loop over buses and invoke bus method, then loop over branches and invoke branch method
void gridpack::powerflow::PFFactory::setYBus(void)
{
int numBus = p_network->numBuses();
int numBranch = p_network->numBranches();
int i;
for (i=0; i<numBus; i++) {
dynamic_cast<PFBus*>(p_network->getBus(i).get())->setYBus();
}
for (i=0; i<numBranch; i++) {
dynamic_cast<PFBranch*>(p_network->getBranch(i).get())->setYBus();
}
}

## Slide 79: Powerflow Main Application
A small “main” program that calls the powerflow application class and executes the simulation. Separates some initialization from the rest of the application and guarantees that objects exit cleanly
The application driver that controls overall program flow and implements the solution algorithm
  Read in network from external configuration file
  Initialize network and set up matrices and vectors
  Implement solution method
  Export results to standard out or to files

## Slide 80: Powerflow “main” Program
Initialize communication libraries (MPI and GA) and math component. Initializing math component invokes initialization routines in underlying math libraries.
Execute application
main(int argc, char **argv)
{
int ierr = MPI_Init(&argc, &argv);
gridpack::math::Initialize();
GA_Initialize();
int stack = 200000, heap = 200000;
MA_init(C_DBL, stack, heap);
gridpack::powerflow::PFApp app;
app.execute();
GA_Terminate();
gridpack::math::Finalize();
ierr = MPI_Finalize();
}

## Slide 81: Powerflow Execution: Setting Up Network
gridpack::parallel::Communicator world;
boost::shared_ptr<PFNetwork> network(new PFNetwork(world));
gridpack::utility::Configuration *config
= gridpack::utility::Configuration::configuration();
config->open("input.xml",world);
gridpack::utility::Configuration::Cursor *cursor;
cursor = config->getCursor("Configuration.Powerflow");
std::string filename = cursor->get("networkConfiguration",
"No network configuration specified");
gridpack::parser::PTI23_parser<PFNetwork> parser(network);
parser.parse(filename.c_str());
network->partition();
Create network
Open input file
Read in name of network configuration file
Read in network
Partition network between processors

## Slide 82: Powerflow Application: Using Factory to Complete Network Initialization
gridpack::powerflow::PFFactory factory(network);
factory.load();
factory.setComponents();
factory.setExchange();
network->initBusUpdate();
factory.setYBus();
Move data from DataCollection objects to bus and branch objects
Set internal indices and buffers
Set up data exchanges between buses
Evaluate Y-matrix components

## Slide 83: Powerflow Application: Creating Mappers and Generating Matrices and Vectors
factory.setMode(YBus);
gridpack::mapper::FullMatrixMap<PFNetwork> mMap(network);
boost::shared_ptr<gridpack::math::Matrix> Y = mMap.mapToMatrix();
factory.setSBus();
factory.setMode(RHS);
gridpack::mapper::BusVectorMap<PFNetwork> vMap(network);
boost::shared_ptr<gridpack::math::Vector> PQ = vMap.mapToVector();
factory.setMode(Jacobian);
gridpack::mapper::FullMatrixMap<PFNetwork> jMap(network);
boost::shared_ptr<gridpack::math::Matrix> J = jMap.mapToMatrix();
boost::shared_ptr<gridpack::math::Vector> X(PQ->clone());
Y-matrix
Right hand side vector
Jacobian
Solution vector

## Slide 84: Powerflow Application: Initialize Newton-Raphson Loop
double tolerance = 1.0e-6;
int max_iteration = 100;
ComplexType tol;
gridpack::math::LinearSolver isolver(*J);
isolver.configure(cursor);
int iter = 0;
X->zero();
isolver.solve(*PQ, *X);
tol = X->norm2();
Set parameters
Set up linear solver an set solver parameters from input file
Solve linear equation and evaluate norm of solution vector

## Slide 85: Powerflow Application: execute Newton-Raphson Iterations
while (real(tol) > tolerance && iter < max_iteration) {
vMap.mapToBus(X);
network->updateBuses();
factory.setMode(RHS);
vMap.mapToVector(PQ);
factory.setMode(Jacobian);
jMap.mapToMatrix(J);
gridpack::math::LinearSolver solver(*J);
solver.configure(cursor);
X->zero();
solver.solve(*PQ, *X);
tol = X->norm2();
iter++;
}
Move solution vector back to buses and exchange data between buses
Create new Jacobian and right hand side vector from updated bus values
Create new linear solver and resolve equations

## Slide 86: Powerflow Application: Export Results to Standard Output
gridpack::serial_io::SerialBusIO<PFNetwork> busIO(128,network);
busIO.header("\n Bus Voltages and Phase Angles\n");
busIO.header("\n Bus Number Phase Angle");
busIO.header(" Voltage Magnitude\n");
busIO.write();
Bus Voltages and Phase Angles
Bus Number Phase Angle Voltage Magnitude
1 0.000000 1.060000
2 -4.982589 1.045000
3 -12.725100 1.010000
4 -10.312901 1.017671
5 -8.773854 1.019514
6 -14.220946 1.070000
7 -13.359627 1.061520
8 -13.359627 1.090000
9 -14.938521 1.055932
10 -15.097288 1.050985
11 -14.790622 1.056907
12 -15.075585 1.055189
13 -15.156276 1.050382
14 -16.033645 1.035530
Write header
Write data from buses